## Slide 1
Izrada 3D modela iz snimljenih fotografija
Autori:
Jasna Čajsa Beber, dipl. ing. geod.
Irena Janton, mag. ing. geod. et geoinf.
Geodetska škola, Zagreb

## Slide 2: 3D modeliranje
3D modeliranje je proces stvaranja 3D prikaza bilo koje površine ili objekta.

## Slide 3: 3D model
3D model je model sa tri dimenzije (x, y i z koordinatna os).

## Slide 4: Fotogrametrija
Fotogrametrija je znanost koja omogućava dobivanje 3D modela iz niza snimaka.

## Slide 5: Fotogrametrija
Ulazni podaci u fotogrametriji su snimke (fotografije).
Fotogrametrijski proizvodi su karte, DMR, 3D modeli terena i objekata.

## Slide 6: Oprema
Za potrebe dobivanja fotografija možemo koristiti bilo koji fotoaparat, kao što je npr. i kamera na mobilnom telefonu.

## Slide 7: Objekt snimanja
Spomenici su pogodni za snimanje zbog mnogo detalja te grublje površine koja sprječava refleksiju.

## Slide 8: Snimanje
Prilikom snimanja, krećemo se u krug oko objekta snimanja.
Snimamo najmanje 20 snimaka, dok je
50 snimaka maksimalan dozvoljen broj snimaka.

## Slide 9: Preklop snimaka
Za izradu modela treba postojati preklop između snimaka od oko 80%.
Svaka nova snimka mora sadržavati 20% novog detalja s obzirom na prethodnu snimku.
Orijentacija kamere uvijek treba biti okomita (vertikalna).

## Slide 10: Kompozicija
Za početak je potrebno izabrati referentnu točku na objektu za orijentaciju pri snimanju.
Glava na spomenku je dobra referenta točka.

## Slide 11: Pozicioniranje objekta na snimku
Objekt bi trebao činiti značajan dio svakog snimka (korištenje zoom-a).

## Slide 12: Što trebamo izbjegavati?
Sjene
Objekte u pokretu
Staklene objekte

## Slide 13: Što trebamo izbjegavati?
Sjene
Potrebno je izbjegavati sjene te po potrebi koristiti dodatni izvor svjetlosti.
Najbolje je snimati na sunčan dan (rano ujutro ili predvečer).

## Slide 14: Što trebamo izbjegavati?
Objekti u pokretu

## Slide 15: Što trebamo izbjegavati?
Stakleni objekti
Svjetlucavi i prozirni objekti mijenjaju izgled i reflektiraju svjetlost.

## Slide 16: Pregled snimljenog materijala
Nakon što snimimo odabrani objekt potrebno je pregledati snimke i obrisati sve koje su zamućene, odnosno nisu oštre.

## Slide 18: Upute za rad u programu 3DF Zephyr
3DF Zephyr je fotogrametrijski program koji omogućava automatsku rekonstrukciju 3D modela pomoću fotografija.
Postupak je u potpunosti automatiziran, ne zahtjeva dodatno kodiranje ni ručnu obradu ili posebnu opremu.

## Slide 19: Cilj
Ove upute su namijenjene za upoznavanje s par jednostavnih naredbi i postupaka za kreiranje 3D modela.

## Slide 20: Preuzimanje snimaka
Potrebno je preuzeti mapu
Snimke_patuljak putem sljedeće poveznice:
bit.ly/3JYDNhR

## Slide 21: Glavno sučelje programa 3DF Zephyr
Nakon što pokrenete program 3DF Zephyr otvara se sljedeći prozor:
Izaberite:
Not now, thank you.

## Slide 22: Kreiranje novog projekta (Starting a New Project)
Imate fotografije? Onda ste spremni za postupak rekonstrukcije 3D modela!
Da biste kreirali novi projekt, izaberite Workflow > New Project (1) .
Prozor Project Wizard (2) (čarobnjak) vodit će vas kroz postupak učitavanja vaših fotografija.

## Slide 23: Kreiranje novog projekta
Izaberite:
Texture
Next

## Slide 24: Učitavanje snimaka
Idući prozor je Photos selection page na kojem korisnici učitavaju svoje snimke:
Moguće je tehnikom drag 'n' drop (uvući) datoteke u prozor ili kliknuti na "+" Button te odabrati datoteke.
Postoji i mogućnost učitavanja cijele mape s datotekama.

## Slide 25: Kalibracija kamere (Camera Calibration)
Nakon učitavanja snimaka kliknite na
Next te će se otvoriti prozor Camera calibration page

## Slide 26: Orijentacija i oblak točaka (Orientation and Point Cloud)
Camera Orientation
Category: Urban
Presets: Deep
Next
Dense Point Cloud Orientation
Category: Urban
Presets: Default
Next

## Slide 27: Rekonstrukcija površine i teksture (Surface and Texturing)
Surface reconstruction
Category: Urban
Presets: Default
Next
Texturing
Category: General
Presets: Default Single Texture
Next

## Slide 28: Rekonstrukcija objekta (Reconstruction)
Start Reconstruction
Run
The software computes Point Cloud and creates the Wire Model

## Slide 29: Kreirani 3D model

## Slide 30: Obrada kreiranog 3D modela (Editing)
Kako bi obrisali neželjene površine, označimo detalj koji želimo ukloniti.

## Slide 31: Obrada kreiranog 3D modela (Editing)

## Slide 32: Kreiranje animacije
Animator
1. Add all cameras positions
2. Play
3. Stop
4. Record

## Slide 33: Snimanje videa (Video Recording)
1. Please Enter the video title:
Prezime_patuljak
2. OK

## Slide 34: Prijava na YouTube
E-pošta: cuc2023.geoskola@gmail.com
Lozinka: geoskola@2023

## Slide 35: Učitavanje videa na YouTube
Naziv videa: Prezime_patuljak

## Slide 36: Spremanje projekta
Naziv projekta: Prezime_patuljak

## Slide 37: Literatura
URL 1. https://www.3dflow.net/technology/documents/3df-zephyr-tutorials (30.4.2021.)
URL 2. https://i.materialise.com/blog/en/how-to-make-a-3d-printed-object-from-a-photo-in-5-easy-steps/ (20.4.2021.)
URL 3. https://www.dronegenuity.com/aerial-photogrammetry/ (21.4.2021.)
URL 4. https://blog.prusaprinters.org/photogrammetry-3d-scanning-just-phone-camera_7811/ (25.4.2021.)

## Slide 38: Hvala na pažnji!